SPARKER TCIP4 - mounting instructions for Yamaha TRX850

Wiring

Wiring must be done according the table below. The wires of ignition SPARKER TCIP4 has various colors. (see table).

| wire color TCIP4 | pin no. TCIP4 | wire color motorbike | name | description |
| --- | --- | --- | --- | --- |
| orange | 1 | grey | IC 1 | ignition coil 1 |
|  | 2 |  | IC 3 | ignition coil 3 |
| violet | 3 | blue/red | FUEL PUMPE RELAY | multifunctional output 1 |
| green | 4 |  | M | output for servomotor |
| green | 5 |  | M | output for servomotor |
| grey | 6 | yellow | TPS | throttle position sensor |
|  | 7 |  |  | ground, ground for sensors |
| black | 8 | black or blue/black (beside blue/yellow) | BLOCK | multifunctional input 1 (used as sidestand block) |
| yellow | 9 | blue/yellow | CKPS (1) | input for pick-up (1) |
| white | 10 | orange | IC 2 | ignition coil 2 |
|  | 11 |  | IC 4 | ignition coil 4 |
|  | 12 |  | GEAR SHIFT LIGHT | multifunctional output 2 |
| red | 13 | red/white | + 12 V | supply 12 V |
| blue | 14 | black | GND | ground |
| green/yellow | 15 | yellow/black | TACHO | output for tachometer light |
| blue | 16 | black/blue | SENSE GND | ground for sensors |
| white/red | 17 | blue | + 5 V | supply for sensors |
| white/blue | 18 |  | STPS | servo position sensor |
|  | 19 |  | CLUTCH MASTER | multifunctional input 2 |
| brown | 20 |  | CKPS (2) | input for pick-up (2) |

Producer address: 	IgniTech

Ceskobratrska 84

535 01 PRELOUC

Czech Republic

ignitech@ignitech.cz

www.ignitech.cz