SPARKER DCCDIP2 - mounting instructions for Honda CR250 with exhaust valve servomotor without TPS.

Wiring

Wiring must be done according the table below. The wires of ignition SPARKER DCCDIP2 has various colors. (see table).

| wire color DCCDIP2 | pin no. DCCDIP2 | wire color motorbike | name | description |
| --- | --- | --- | --- | --- |
| grey/black | 1 |  | INPUT 3 | multifunction input |
| white/black | 2 |  | POT | correction potentiometer (analog input) |
| green/yellow | 3 |  | TACHO | tachometer output |
| blue | 4 | green | GND | power ground |
| red | 5 | red | SUPPLY +12V | supply +12 V |
| violet | 6 |  | POWER OUT 1 | power out 1 (fuel pump relay) |
| blue/white | 7 |  | POWER OUT 2 | power out 2 (gear shift light) |
| pink | 8 |  | POWER OUT 3 | power out 3 (POWER JET Honda) |
| orange | 9 | black/yellow | IC | ignition coil |
| blue | 10 | green/white | GND | power ground |
|  | 11 |  | NC | not connected |
| black | 12 |  | INPUT 2 | multifunction input 2 |
|  | 13 |  | NC | not connected |
| red/black | 14 |  | AC SUPPLY | main ac supply |
| red/black | 15 |  | AC SUPPLY | main ac supply |
|  | 16 |  | NC | not connected |
| yellow/black | 17 |  | AC SUPPLY | auxiliary ac supply |
|  | 18 |  | NC | not connected |
| grey/red | 19 | black/white | INPUT 1 | multifunction input 1 |
|  | 20 |  | NC | not connected |
| white/red | 21 | yellow/red | + 5V | supply +5V for sensors |
| black | 22 |  | Comm | RS232 (pin 2 in 9pin connector) |
| yellow | 23 |  | Comm | RS232 (pin 3 in 9pin connector) |
| violet | 24 |  | Comm | RS232 connector (pin 1 in 9pin connector) |
| orange | 25 |  | Comm | RS232 connector (pin 9 in 9pin connector) |
| blue | 26 |  | 232GND | ground for RS232 (pin 5 in 9pin connector) |
| yellow | 27 | blue/yellow | PICK-UP | pickup |
| white/red | 28 |  | + 5V | supply +5V for sensors |
| grey | 29 |  | TPS | throttle position sensor input |
| blue | 30 | blue/green | SENSE GND | ground for sensors |
| white/blue | 31 | light green | STPS | servomotor position sensor input |
| green | 32 | white/black | M+ | output for servomotor |
| green | 33 | white/green | M- | output for servomotor |
|  | 34 |  | NC | not connected |

Producer address: 	IgniTech

Ceskobratrska 84

535 01 PRELOUC

Czech Republic

ignitech@ignitech.cz

www.ignitech.cz