SPARKER DC-CDI - mounting instructions for Suzuki DR650R (without el. starter)

Wiring

Wiring must be done according the table below. The wires of ignition SPARKER DC-CDI has various colors. (see table).

| SPARKER DC-CDI | motorbike | original unit | note |
| --- | --- | --- | --- |
| blue | green/white | green | sensor ground |
| yellow | blue/white | orange | CKPS |
| black | green | green | side stand switch |
| grey | blue | blue | neutral switch |
| grey | blue/black | blue/black | pilot-light neutral |
| red |  |  | key switched + 12 V |
| blue | black/white | black/white | ground |
| blue | brown | brown | charging coil |
| orange | black | black | induction coil |
| green | black/yellow | black/yellow | engine stop switch |

or

| SPARKER DC-CDI | motorbike | original unit | note |
| --- | --- | --- | --- |
| blue | green/white | green/white | sensor ground |
| yellow | blue/white | blue/white | CKPS |
| black | green | green | side stand switch |
| grey | blue | blue | neutral switch |
| grey | blue/black | blue/black | pilot-light neutral |
| red |  |  | key switched + 12 V |
| blue | black/white | black/white | ground |
| blue | brown | brown | charging coil |
| orange | black | black | induction coil |
| green | black/yellow | black/yellow | engine stop switch |

Producer address: 	IgniTech

Chrudimská 1739

535 01 PRELOUC

Czech Republic

ignitech@ignitech.cz

www.ignitech.cz