SPARKER DCCDIP2 - mounting instructions for Aprilia RS125 2008

Wiring

Wiring must be done according the table below. The wires of ignition SPARKER DCCDIP2 has various colors. (see tables). Counterpart connectors are included.

| pin no. DCCDIP2 | wire color motorbike | name | description |
| --- | --- | --- | --- |
| 1 | white/violet | IC 1 | inductive coil 1 |
| 2 | blue | GND | ground (use for pickup gnd) |
| 3 | white/red | POWEROUT 1 | use for fuel switch |
| 4 |  | M | output for servomotor |
| 5 |  | M | output for servomotor |
| 6 | yellow/brown | TPS | throttle position sensor |
| 7 |  |  |  |
| 8 | white/blue | INPUT 2 | use for BLOCKING |
| 9 | yellow/blue | PICK-UP 1 | input for pick-up 1 |
| 10 |  | IC 2 | inductive coil 2 |
| 11 |  | GND | power ground |
| 12 | white | POWEROUT 2 | use for exhaust valve elmag |
| 13 | red/black (in 14pin connector), orange (in 3pin connector) | + 12 V | supply 12 V |
| 14 |  | POWEROUT 3 | power output 3 |
| 15 | white/yellow | TACHO | output for tachometer |
| 16 | grey (in 3pin connector) | SENSE GND | ground for sensors |
| 17 | white/brown | + 5 V | supply for sensors |
| 18 |  | STPS | servo position sensor |
| 19 |  | INPUT 1 | multifunctional input 1 |
| 20 |  | PICK-UP 2 | input for pick-up 2 |

Interconnect orange/blue (in 3pin connector) with yellow/pink (in 14pin connector) without connection to unit DCCDIP2.