SPARKER DCCDIP2 - mounting instructions for Honda CM400 CB400N CB400T

Wiring

Wiring must be done according the table below. The wires of ignition SPARKER DCCDIP2 has various colors. (see table). Counterpart connectors are included.

| wire color DCCDIP2 | pin no. DCCDIP2 | wire color motorbike | name | description |
| --- | --- | --- | --- | --- |
| orange | 1 | yellow | IC 1 | inductive coil 1 |
| blue | 2 | green | SENSE GND | ground for sensors |
| violet | 3 |  | FUEL PUMPE RELAY | output for fuel pump relay |
| green | 4 |  | M | output for servomotor |
| green | 5 |  | M | output for servomotor |
| grey | 6 |  | TPS | throttle position sensor |
|  | 7 |  |  |  |
| black | 8 |  | INPUT 1 | multifunctional input 1 |
| yellow | 9 | light blue | CKPS (1) | input for pick-up (1) |
| white | 10 |  | IC 2 | inductive coil 2 |
| blue | 11 | green | GND | ground |
| violet | 12 |  | GEAR SHIFT LIGHT | output for gear shift light |
| red | 13 | black from main switch | + 12 V | supply 12 V |
| pink | 14 |  | POWER JET | Power jet output |
| green/yellow | 15 |  | TACHO | output for tachometer |
| blue | 16 |  | GND | ground |
| white/red | 17 |  | + 5 V | supply for sensors |
| white/blue | 18 |  | STPS | servo position sensor |
| grey/red | 19 | black/white | INPUT 2 | multifunctional input 1 (used as KILL switch) |
| brown | 20 | brown | CKPS (2) | input for pick-up (2) |

Producer address: 	IgniTech

Chrudimská 1739

535 01 PRELOUC

Czech Republic

ignitech@ignitech.cz

www.ignitech.cz