SPARKER DCCDIP2 - mounting instructions for Honda CR250

Wiring

Wiring must be done according the table below. The wires of ignition SPARKER DCCDIP2 has various colors. (see table). Counterpart connectors are included.

| wire color DCCDIP2 | pin no. DCCDIP2 | wire color motorbike | name | description |
| --- | --- | --- | --- | --- |
| orange | 1 | black/yellow | IC 1 | inductive coil 1 |
| blue | 2 | green/white | SENSE GND | ground for sensors |
| violet | 3 |  | FUEL PUMPE RELAY | output for fuel pump relay |
| green | 4 |  | M | output for servomotor |
| green | 5 |  | M | output for servomotor |
| grey | 6 |  | TPS | throttle position sensor |
|  | 7 |  | BLOCK_A | blocking input (neutral sw.) |
| black | 8 |  | BLOCK | blocking input (sidetand sw.) |
| yellow | 9 | blue/yellow | CKPS (1) | input for pick-up (1) |
| white | 10 |  | IC 2 | inductive coil 2 |
| blue | 11 | green | GND | ground |
|  | 12 |  | GEAR SHIFT LIGHT | output for gear shift light |
| red | 13 |  | + 12 V | supply 12 V |
|  | 14 |  | POWER JET | Power jet output |
| green/yellow | 15 |  | TACHO | output for tachometer |
|  | 16 |  |  |  |
| white/red | 17 |  | + 5 V | supply for sensors |
| white/blue | 18 |  | STPS | servo position sensor |
|  | 19 | black/white | KILL SWITCH | input for kill switch |
| brown | 20 |  | CKPS (2) | input for pick-up (2) |

Producer address: 	IgniTech

Ceskobratrska 84

535 01 PRELOUC

Czech Republic

ignitech@ignitech.cz

www.ignitech.cz