SPARKER DCCDIP2 - mounting instructions for Honda CX500

Wiring

Wiring must be done according the table below. The wires of ignition SPARKER DCCDIP2 has various colors. (see tables).

| wire color DCCDIP2 | pin no. DCCDIP2 | wire color motorbike | name | description |
| --- | --- | --- | --- | --- |
| orange | 1 | pink | IC 1 | inductive coil 1 (right) |
| blue | 2 | blue | GND | ground (used for grounding of HV supply) |
|  | 3 |  | POWEROUT 1 | power output 1 |
|  | 4 |  | M | output for servomotor |
|  | 5 |  | M | output for servomotor |
|  | 6 |  | TPS | throttle position sensor |
|  | 7 |  |  |  |
|  | 8 |  | INPUT 2 | multifunctional input 2 |
| 2x yellow | 9 | light green, light green/red | PICK-UP 1 | input for pick-up 1 |
| white | 10 | yellow | IC 2 | inductive coil 2 (left) |
| blue | 11 | green | GND | power ground |
|  | 12 |  | POWEROUT 2 | power output 2 |
| red | 13 | black (from ignition key) | + 12 V | supply 12 V |
|  | 14 |  | POWEROUT 3 | power output 3 |
|  | 15 |  | TACHO | output for tachometer |
| blue | 16 | white | GND | ground (used for grounding of HV supply) |
|  | 17 |  | + 5 V | supply for sensors |
|  | 18 |  | STPS | servo position sensor |
| green (grey/red) | 19 | black/white | INPUT 1 | multifunctional input 1 (used for kill switch |
| 2x brown | 20 | orange, orange/red | PICK-UP 2 | input for pick-up 2 |

Supply +12V (two red wires) is possible connect to black wire on foot brake switch (insert to connector of foot brake switch).

Here is short connect manual movie: http://www.youtube.com/watch?v=XEEiB65FznM

Here is detailed connection description : http://cx500info.com/install-ignitech-cx500-dccdip2/

Producer address: 	IgniTech

Chrudimská 1739

535 01 PRELOUC

Czech Republic

ignitech@ignitech.cz

www.ignitech.cz