SPARKER DCCDIP2 - mounting instructions for Kawasaki KFX700, KVF700

Wiring

Wiring must be done according the table below. The wires of ignition SPARKER DCCDIP2 has various colors. (see tables). Counterpart connectors are included.

| wire color DCCDIP2 | pin no. DCCDIP2 | wire color motorbike | name | description |
| --- | --- | --- | --- | --- |
| orange | 1 | blue/white | IC 1 | inductive coil 1 |
| blue | 2 | black/white | SENSE GND | ground for sensors |
| violet | 3 | black/red | FUEL PUMPE RELAY | output for fuel pump relay |
|  | 4 |  | M | output for servomotor |
|  | 5 |  | M | output for servomotor |
|  | 6 |  | TPS | throttle position sensor |
|  | 7 |  | INPUT 2A | input 2 (through diode) |
| black | 8 | yellow/green | INPUT 2 | input 2 |
| yellow | 9 | blue | CKPS (1) | input for pick-up (1) |
| white | 10 | green/white | IC 2 | inductive coil 2 |
| blue | 11 | black/yellow | GND | ground |
| white/red | 12 | white/red | GEAR SHIFT LIGHT | output for gear shift light (use to belt indicator) |
| red | 13 | yellow/red | + 12 V | supply 12 V |
|  | 14 |  | POWER OUT 3 | Power output 3 |
|  | 15 |  | TACHO | output for tachometer |
|  | 16 |  |  |  |
|  | 17 |  | + 5 V | supply for sensors |
|  | 18 |  | STPS | servo position sensor |
| grey | 19 | red/white | INPUT 1 | input 1 (use for reverse limiter) |
|  | 20 |  | CKPS (2) | input for pick-up (2) |