SPARKER DCCDIP2 - mounting instructions for Rotax 912/914

Wiring

Wiring must be done according the table below. The wires of ignition SPARKER DCCDIP2 has various colors. (see table).

1) 6+6 pins connectors (912 A/F/UL/ULS/S, 914 UL/F)

2) 6+4+1 pins connectors (912 ULS/S)

3) 4 pins connector + 7 separate wires (912 A/F/UL)

4) 4 pins connector + 5 separate wires (914 UL/F)

| wire color DCCDIP2 | pin no. DCCDIP2 | wire color airplane | name | description |
| --- | --- | --- | --- | --- |
| orange | 1 | yellow (or second white) | IC 1 | ignition coil 1 |
| 2x blue | 2 | 2x blue (or 2x black) | GND | ground for ignition coils |
|  | 3 |  | POWEROUT 1 | poweroutput 1 |
|  | 4 |  | M | output for servomotor |
|  | 5 |  | M | output for servomotor |
|  | 6 |  | TPS | throttle position sensor |
|  | 7 |  |  | reserve |
|  | 8 |  | INPUT 2 | multifunctional input 2 |
| yellow | 9 | blue/yellow | CKPS (1) | input for pick-up 1 |
| white | 10 | white | IC 2 | ignition coil 2 |
| blue, blue from preregulator | 11 | black | GND | ground from preregulator |
|  | 12 |  | POWEROUT 2 | poweroutput 2 |
| red from preregulator | 13 |  | + 12 V | supply 12 V from preregulator |
|  | 14 |  | POWEROUT 3 | poweroutput 3 |
|  | 15 |  | TACHO | output for tachometer |
| 2x light blue | 16 | 2x white/yellow | GND | ground for pickups |
|  | 17 |  | + 5 V | supply for sensors |
|  | 18 |  | STPS | servo position sensor |
| grey/red | 19 | brown | INPUT 1 | multifunctional input 1 (kill switch) |
|  | 20 | blue/yellow | CKPS (2) | input for pick-up 2 |
| yellow/black |  | red | AC | AC voltage to preregulator |
| red/black |  |  | +12 V to preregulator | +12 V from key switch |

Producer address: 	IgniTech

Chrudimská 1739

535 01 PRELOUC

Czech Republic

ignitech@ignitech.cz

www.ignitech.cz