SPARKER DCCDIP2 - mounting instructions for Yamaha RD350

Wiring

Wiring must be done according the table below. The wires of ignition SPARKER DCCDIP2 has various colors. (see table).

| wire color DCCDIP2 | pin no. DCCDIP2 | wire color motorbike | name | description |
| --- | --- | --- | --- | --- |
|  | 1 | orange | IC 1 | inductive coil 1 |
|  | 2 | white/green (on CDI unit) white/black (on YPVS motor) | SENSE GND | ground for sensors |
|  | 3 |  | FUEL PUMPE RELAY | output for fuel pump relay |
|  | 4 | black/red (on YPVS motor) | M | output for servomotor |
|  | 5 | black/yellow (on YPVS motor) | M | output for servomotor |
|  | 6 |  | TPS | throttle position sensor |
|  | 7 |  | BLOCK_A | blocking input (neutral sw.) |
|  | 8 |  | BLOCK | blocking input (sidetand sw.) |
|  | 9 | white/red (on CDI unit) | CKPS (1) | input for pick-up (1) |
|  | 10 |  | IC 2 | inductive coil 2 |
|  | 11 | black (on CDI unit) | GND | ground |
|  | 12 |  | GEAR SHIFT LIGHT | output for gear shift light |
|  | 13 | brown (from ignition key) | + 12 V | supply 12 V |
|  | 14 |  | POWER JET | Power jet output |
|  | 15 |  | TACHO | output for tachometer |
|  | 16 |  |  |  |
|  | 17 | yellow/blue (on YPVS motor) | + 5 V | supply for sensors |
|  | 18 | white/red (on YPVS motor) | STPS | servo position sensor |
|  | 19 |  | KILL SWITCH | input for kill switch |
|  | 20 |  | CKPS (2) | input for pick-up (2) |
| violet | separate wire | black/white or black/yellow | YPVS and TACHO trigger | trigger output for YPVS unit and TACHOMETER |

Residual wires no connect !!!

Producer address: 	IgniTech

Chrudimská 1739

535 01 PRELOUC

Czech Republic

ignitech@ignitech.cz

www.ignitech.cz