SPARKER TCI - mounting instructions for Moto Guzzi Nevada 750

Motorbike Moto Guzzi Nevada 750 has the inductive ignition with electronic regulation of ignition advance DIGIPLEX Magnetti Marelli (see to picture).

Wiring

Wiring must be done according the table below. The wires of ignition SPARKER TCI has various colors. (see table). Counterpart connectors are included.

| SPARKER TCI | pin no. DIGIPLEX Magnetti Marelli) | note |
| --- | --- | --- |
| yellow | 2 | sensor (+) |
| blue | 1 | sensor ground (-) |
| red | 6 | key switched + 12 V |
| blue | 10 | ground |
| white | 9 | induction coil L |
| orange | 11 | induction coil R |

Producer address: 	IgniTech

Ceskobratrska 84

535 01 PRELOUC

Czech Republic

ignitech@ignitech.cz

www.ignitech.cz