Ignition SPARKER TCI - Universal mounting instructions for 1, 2 or 4 - cylinder bike with classic pick-up system.

Ignition SPARKER TCI is the inductive ignition.

Recommend wiring for Ignition SPARKER TCI is below. Wires of ignition provided with two connectors. The wires of ignition has various colors:

red		supply +12 V

3x blue		ground

orange		IC 1, 4

white		IC 2, 3

yellow		pick-up 1, 4

brown		pick-up 2, 3

black		blocking input

Pick-up connection

Outlets of sensor should be connected that way, that if lobe of rotor is approaching the voltage is positive and if the lobe is  departing the voltage is negative (to ground). If you are using pick-up sensor VAPE S01, you nedn’t take care of polarity of pick-up. (VAPE pick-up has one outlets grounded inside).

Pick up sensors must be placed so as ignition sparks into proper induction coil.

Pick up sensors may not be placed so as the lobe don’t interfere with both pick-up sensors in the same time.

Connection of induction coils

Induction coils used by SPARKER TCI must be for induction ignition. Induction coils must be connected to +12 V. Resistance of  primary coil must be min. 2.2 Ohm. Using induction coils with smaller resistance can cause damage of ignition or induction coils.

Connection of inhibit input

Inhibit input is used for interlocking of ignition by side stand switch or alarm device etc. Ignition is disabled if inhibit input (black) is not connect to ground. The ignition is equipted with inhibit input only as options - default ignition is without inhibit input.

Advance control

Ignition advance as function of rpm (speed) can be maked according request of customer. Default setting is on figure below.

The ignition is equipted with limiter of revolutions input only as options - default ignition is without limiter.

If the pick-up system is on  camshaft it  must be mentioned in order, default is pick-up system on crankshaft.

Scheme:

Address: 	IgniTech s.r.o.

Ceskobratrska 84

535 01 PRELOUC

ignitech@ignitech.cz

www.ignitech.cz