SPARKER TCIP4 - mounting instructions for Kawasaki ZX6RR (2005-2006) - replacement from injection to carburators

Wiring

Wiring must be done according the table below. The wires of ignition SPARKER TCIP4 has various colors. (see table).

| wire color TCIP4 | pin no. TCIP4 | wire color 34pin connector | wire color 26pin connector | name | description |
| --- | --- | --- | --- | --- | --- |
| orange | 1 |  | black | IC 1 | inductive coil 1 |
| yellow/black | 2 |  | black/white | IC 3 | inductive coil 3 |
| violet | 3 |  | brown/yellow | FUEL PUMPE RELAY | output for fuel pump relay |
| green | 4 | green/red |  | M | output for servomotor |
| green | 5 | grey |  | M | output for servomotor |
| grey | 6 |  |  | TPS | throttle position sensor |
| blue | 7 |  | black/yellow | GND | ground |
| black | 8 |  |  | INPUT 1 | multifunctional input 1 |
| yellow | 9 | yellow/red |  | CKPS (1) | input for pick-up (1) - use for CAM |
| white | 10 |  | black/green | IC 2 | inductive coil 2 |
| red/black | 11 |  | black/orange | IC 4 | inductive coil 4 |
| green/black | 12 |  |  | GEAR SHIFT LIGHT | output for gear shift light |
| red | 13 |  | red | + 12 V | supply 12 V |
| blue | 14 |  | black/yellow | GND | ground |
| green/yellow | 15 |  | light blue | TACHO | output for tachometer |
| blue | 16 | brown/black brown/white black |  | SENSE GND | ground for sensors |
| white/red | 17 | blue |  | + 5 V | +5V supply for sensors |
| white/blue | 18 | red/black |  | STPS | servo position sensor |
| grey/red | 19 |  |  | INPUT 2 | multifunctional input 2 |
| brown | 20 | yellow/black |  | CKPS (2) | input for pick-up (2) -use for CRANK |

Producer address: 	IgniTech

Ceskobratrska 84

535 01 PRELOUC

Czech Republic

ignitech@ignitech.cz

www.ignitech.cz