SPARKER TCIP4 - mounting instructions for Suzuki GSX600R (from 2008) - replacement from injection to carburators

Wiring

Wiring must be done according the table below. The wires of ignition SPARKER TCIP4 has various colors. (see table).

| wire color TCIP4 | pin no. TCIP4 | wire color grey connector | wire color black connector | name | description |
| --- | --- | --- | --- | --- | --- |
| orange | 1 | white/blue |  | IC 1 | inductive coil 1 |
| yellow/black | 2 | yellow |  | IC 3 | inductive coil 3 |
| violet | 3 | yellow/black |  | FUEL PUMPE RELAY | output for fuel pump relay |
| green | 4 |  | black/red | M | output for servomotor |
| green | 5 |  | red/black | M | output for servomotor |
| grey | 6 |  |  | TPS | throttle position sensor |
| blue | 7 |  | black/white | GND | ground |
| black | 8 |  |  | INPUT 1 | multifunctional input 1 |
| yellow | 9 |  | black/yellow | CKPS (1) | input for pick-up (1) - use for CAM |
| white | 10 | black |  | IC 2 | inductive coil 2 |
| red/black | 11 | green |  | IC 4 | inductive coil 4 |
| green/black | 12 |  |  | GEAR SHIFT LIGHT | output for gear shift light |
| red | 13 |  | orange/green | + 12 V | supply 12 V |
| blue | 14 | black/white |  | GND | ground |
| green/yellow | 15 |  | yellow/blue | TACHO | output for tachometer |
| blue | 16 |  | black/brown green/blue | SENSE GND | ground for sensors |
| white/red | 17 |  | red | + 5 V | +5V supply for sensors |
| white/blue | 18 |  | yellow | STPS | servo position sensor |
| grey/red | 19 |  |  | INPUT 2 | multifunctional input 2 |
| brown | 20 |  | green/white | CKPS (2) | input for pick-up (2) -use for CRANK |

Producer address: 	IgniTech

Chrudimská 1739

535 01 PRELOUC

Czech Republic

ignitech@ignitech.cz

www.ignitech.cz