SPARKER TCIP4 - mounting instructions for Yamaha YZF-R1 (2002-2003) - replacement from injection to carburators

Wiring

Wiring must be done according the table below. The wires of ignition SPARKER TCIP4 has various colors. (see table).

| wire color TCIP4 | pin no. TCIP4 | wire color motorbike | pin no. original unit | name | description |
| --- | --- | --- | --- | --- | --- |
| orange | 1 | orange | 1 | IC 1 | inductive coil 1 |
| yellow/black | 2 | orange/green | 23 | IC 3 | inductive coil 3 |
| violet | 3 | blue/yellow | 32 | FUEL PUMPE RELAY | output for fuel pump relay |
| green | 4 | black/green | 20 | M | output for servomotor |
| green | 5 | black/red | 22 | M | output for servomotor |
| grey | 6 | yellow | 19 | TPS | throttle position sensor |
| blue | 7 | black | 25 | GND | ground |
| black | 8 |  |  | INPUT 1 | multifunctional input 1 |
| yellow | 9 | white/black | 12 | CKPS (1) | input for pick-up (1) - use for CAM |
| white | 10 | grey/red | 2 | IC 2 | inductive coil 2 |
| red/black | 11 | grey/green | 24 | IC 4 | inductive coil 4 |
| green/black | 12 |  |  | GEAR SHIFT LIGHT | output for gear shift light |
| red | 13 | red/white | 15 | + 12 V | supply 12 V |
| blue | 14 | black | 3 | GND | ground |
| green/yellow | 15 | yellow/black | 4 | TACHO | output for tachometer |
| blue | 16 | black/blue | 34 | SENSE GND | ground for sensors |
| white/red | 17 | blue | 10 | + 5 V | +5V supply for sensors |
| white/blue | 18 | white/red | 44 | STPS | servo position sensor |
| grey/red | 19 |  |  | INPUT 2 | multifunctional input 2 |
| brown | 20 | grey | 30 | CKPS (2) | input for pick-up (2) -use for CRANK |

Producer address: 	IgniTech

Chrudimská 1739

535 01 PRELOUC

Czech Republic

ignitech@ignitech.cz

www.ignitech.cz