SPARKER TCIP4 - mounting instructions for Dyna 2000 pickup system.

Wiring

Wiring must be done according the table below. The wires of ignition SPARKER TCIP4 has various colors. (see table). Counterpart connectors are included.

| wire color TCIP4 | pin no. TCIP4 | wire color motorbike | name | description |
| --- | --- | --- | --- | --- |
| orange | 1 |  | IC 1 | ignition coil 1 |
| yellow/black | 2 |  | IC 3 | ignition coil 3 |
| violet | 3 |  | POWEROUT 1 | multifunctional output 1 |
| green | 4 |  | M | output for servomotor |
| green | 5 |  | M | output for servomotor |
| grey | 6 |  | TPS | throttle position sensor |
| blue | 7 |  | GND, SENSE GND | ground, ground for sensors |
| black | 8 |  | INPUT1 | multifunctional input 1 |
| yellow | 9 | white | CKPS (1) | input for pick-up (1) |
| white | 10 |  | IC 2 | ignition coil 2 |
| red/black | 11 |  | IC 4 | ignition coil 4 |
| blue/white | 12 |  | POWEROUT 2 | multifunctional output 2 |
| red | 13 |  | + 12 V | supply 12 V |
| blue | 14 |  | GND | ground |
| green/yellow | 15 |  | TACHO | output for tachometer light |
| blue | 16 | black | SENSE GND | ground for sensors |
| white/red | 17 | red | + 5 V | supply for sensors |
| white/blue | 18 |  | STPS | servo position sensor |
| grey/red | 19 |  | INPUT2 | multifunctional input 2 |
| brown | 20 | blue | CKPS (2) | input for pick-up (2) |

Producer address: 	IgniTech

Ceskobratrska 84

535 01 PRELOUC

Czech Republic

ignitech@ignitech.cz

www.ignitech.cz