SPARKER TCIP4 - mounting instructions for Honda CBR600F

1987-1990 (pick-up system 7lobes)

Wiring

Wiring must be done according the table below. The wires of ignition SPARKER TCIP4 has various colors. (see table). Counterpart connectors are included.

| wire color TCIP4 | pin no. TCIP4 | wire color motorbike | name | description |
| --- | --- | --- | --- | --- |
| orange | 1 | yellow/blue | IC 1 | inductive coil 1,4 |
|  | 2 |  | IC 3 | not connected in standard |
| violet | 3 |  | FUEL PUMPE RELAY | output for fuel pump relay |
| green | 4 |  | M | output for servomotor |
| green | 5 |  | M | output for servomotor |
| grey | 6 |  | TPS | throttle position sensor |
|  | 7 |  |  | not connected |
| black | 8 |  | INPUT1 | multifunctional input 1 |
| yellow | 9 | yellow | CKPS (1) | input for pick-up (1) |
| white | 10 | blue/yellow | IC 2 | inductive coil 2,3 |
|  | 11 |  | IC 4 | not connected in standard |
|  | 12 |  | GEAR SHIFT LIGHT | output for gear shift light |
| red | 13 | black/white | + 12 V | supply 12 V |
| blue | 14 | green | GND | ground |
| green/yellow | 15 |  | TACHO | output for tachometer |
| blue | 16 | white/blue, white/yellow | SENSE GND | ground for sensors |
| white/red | 17 |  | + 5 V | supply for sensors |
| white/blue | 18 |  | STPS | servo position sensor |
|  | 19 |  | INPUT2 | multifunctional input 2 |
| brown | 20 | blue | CKPS (2) | input for pick-up (2) |

Producer address: 	IgniTech

Ceskobratrska 84

535 01 PRELOUC

Czech Republic

ignitech@ignitech.cz

www.ignitech.cz