SPARKER TCIP4 - mounting instructions for Yamaha KTM690 (model with one spark plug)

Wiring

Wiring must be done according the table below. The wires of ignition SPARKER TCIP4 has various colors. (see table).

| wire color TCIP4 | pin no. TCIP4 | wire color motorbike | name | description |
| --- | --- | --- | --- | --- |
| orange | 1 | white/violet | IC 1 | inductive coil 1,4 |
|  | 2 |  | IC 3 | not connected in standard |
|  | 3 |  | POWER OUT 1 | multifunctional output 1 |
|  | 4 |  | M | output for servomotor |
|  | 5 |  | M | output for servomotor |
|  | 6 |  | TPS | throttle position sensor |
|  | 7 |  | SENSE GND | ground for sensors |
|  | 8 |  | INPUT 1 | multifunctional input 2 |
|  | 9 |  | CKPS (1) | input for pick-up (1) |
|  | 10 |  | IC 2 | inductive coil 2,3 |
|  | 11 |  | IC 4 | not connected in standard |
|  | 12 |  | POWER OUT 2 | multifunctional output 2 |
| red | 13 | yellow/red | + 12 V | supply 12 V (from handlebar) |
| blue | 14 | brown | GND | ground |
|  | 15 |  | TACHO | output for tachometer light |
| blue | 16 | yellow/blue | SENSE GND | ground for sensors |
|  | 17 |  | + 5 V | supply for sensors |
|  | 18 |  | STPS | servo position sensor |
|  | 19 |  | INPUT 2 | multifunctional input 2 |
| brown | 20 | white/yellow | CKPS (2) | input for pick-up (2) |

Producer address: 	IgniTech

Chrudimská 1739

535 01 PRELOUC

Czech Republic

ignitech@ignitech.cz

www.ignitech.cz