SPARKER TCIP4 - mounting instructions for Kawasaki VN750

Wiring

Wiring must be done according the table below. The wires of ignition SPARKER TCIP4 has various colors. (see table).

| wire color TCIP4 | pin no. TCIP4 | wire color motorbike | name | description |
| --- | --- | --- | --- | --- |
| orange | 1 | black (in 6pin connector) | IC 1 | inductive coil 2 |
|  | 2 |  | IC 3 | inductive coil 3 |
|  | 3 |  | FUEL PUMPE RELAY | output for fuel pump relay |
|  | 4 |  | M | output for servomotor |
|  | 5 |  | M | output for servomotor |
|  | 6 |  | TPS | throttle position sensor |
| blue | 7 | black/red | SENSE GND | ground for sensors |
| black | 8 | black/white (in 6pin connector) | INPUT 1 | multifunctional input (BLOCK) |
| yellow | 9 | black (in 4pin connector) | CKPS (1) | input for pick-up (1) |
| white | 10 | green | IC 2 | inductive coil 1 |
|  | 11 |  | IC 4 | inductive coil 4 |
|  | 12 |  | GEAR SHIFT LIGHT | output for gear shift light |
| red | 13 | red | + 12 V | supply 12 V |
| blue | 14 | black/yellow (in 6pin connector) | GND | ground |
|  | 15 |  | TACHO | output for tachometer 2p/rev |
| blue | 16 | black/yellow (in 4pin connector) | SENSE GND | ground for sensors |
|  | 17 |  | + 5 V | supply for sensors |
|  | 18 |  | STPS | servo position sensor |
|  | 19 |  | INPUT 2 | multifunctional input |
| brown | 20 | black/white (in 4pin connector) | CKPS (2) | input for pick-up (2) |

Producer address: 	IgniTech

Ceskobratrska 84

535 01 PRELOUC

Czech Republic

ignitech@ignitech.cz

www.ignitech.cz