SPARKER TCIP4 - mounting instructions for Kawasaki ZX6R 2000

Wiring

Wiring must be done according the table below. The wires of ignition SPARKER TCIP4 has various colors. (see table).

| wire color TCIP4 | pin no. TCIP4 | wire color motorbike | name | description |
| --- | --- | --- | --- | --- |
| orange | 1 | white/red | IC 1 | inductive coil 2 |
| orange | 2 | white/green | IC 3 | inductive coil 3 |
| violet | 3 |  | FUEL PUMPE RELAY | output for fuel pump relay |
| green | 4 |  | M | output for servomotor |
| green | 5 |  | M | output for servomotor |
| grey | 6 | yellow/white | TPS | throttle position sensor |
|  | 7 |  |  | not connected |
| black | 8 | green/black | BLOCK | blocking input |
| yellow | 9 |  | CKPS (1) | input for pick-up (1) |
| white | 10 | white/blue | IC 2 | inductive coil 1 |
| white | 11 | white/yellow | IC 4 | inductive coil 4 |
|  | 12 |  | GEAR SHIFT LIGHT | output for gear shift light |
| red | 13 | brown/white | + 12 V | supply 12 V |
| blue | 14 | black/yellow | GND | ground |
| green/yellow | 15 | light blue | TACHO | output for tachometer 2p/rev |
| blue | 16 | black/blue | SENSE GND | ground for sensors |
| white/red | 17 | blue | + 5 V | supply for sensors |
| white/blue | 18 |  | STPS | servo position sensor |
|  | 19 |  | CLUTCH MASTER | input for gear shift sensor |
| brown | 20 | black/white | CKPS (2) | input for pick-up (2) |

Producer address: 	IgniTech

Ceskobratrska 84

535 01 PRELOUC

Czech Republic

ignitech@ignitech.cz

www.ignitech.cz