SPARKER TCIP4 - mounting instructions for Moto Guzzi

(original Digiplex unit)

Motorbike Moto Guzzi Nevada 750 has the inductive ignition with electronic regulation of ignition advance DIGIPLEX Magnetti Marelli (see to picture).

Wiring

Wiring must be done according the table below. The wires of ignition SPARKER TCIP4 has various colors. (see table).

| wire TCIP4 | pin TCIP4 | pin original unit | wire original unit | name | description |
| --- | --- | --- | --- | --- | --- |
| orange | 1 | 11 | yellow/black | IC 1 | inductive coil 1,4 |
|  | 2 |  |  | IC 3 | not connected in standard |
|  | 3 |  |  | FUEL PUMPE RELAY | output for fuel pump relay |
|  | 4 |  |  | M | output for servomotor |
|  | 5 |  |  | M | output for servomotor |
| grey | 6 |  |  | TPS, IAPS | engine load sensor |
| blue | 7 |  |  | SENSE GND | ground for sensors |
|  | 8 |  |  | BLOCK | multifunctional input 1 |
| yellow | 9 | 2 | black | CKPS (1) | input for pick-up (1) |
| white | 10 | 9 | light green | IC 2 | inductive coil 2,3 |
|  | 11 |  |  | IC 4 | not connected in standard |
|  | 12 |  |  | GEAR SHIFT LIGHT | output for gear shift light |
| red | 13 | 6 | white/red | + 12 V | supply 12 V |
| blue | 14 | 10 | black | GND | ground |
|  | 15 |  |  | TACHO | output for tachometer |
| blue | 16 | 1 | black | SENSE GND | ground for sensors |
| white/red | 17 |  |  | + 5 V | supply for sensors |
|  | 18 |  |  | STPS | servo position sensor |
|  | 19 |  |  | CLUTCH MASTER | multifunctional input 2 |
|  | 20 |  |  | CKPS (2) | input for pick-up (2) |

Producer address: 	IgniTech

Chrudimská 1739

535 01 PRELOUC

Czech Republic

ignitech@ignitech.cz

www.ignitech.cz