SPARKER TCIP4 - mounting instructions for Suzuki GS450

Motorbike GS450 has the inductive ignition with centrifugal regulation of ignition advance.

There are two possibilities:

a) Application with original centrifugal advance regulator.

You must use appropriate setting for use with centrifugal advance regulator. Appropriate setting is on delivered CD.

b) Application with centrifugal advance regulator fixate in idle position.

You must fixating movable part of pulse rotor in idle position.

You must use appropriate setting for use with centrifugal advance regulator fixate in idle position. Appropriate setting is on delivered CD.

Wiring

Wiring must be done according the table below. The wires of ignition SPARKER TCIP4 has various colors. (see table). Counterpart connectors are included.

| wire color TCIP4 | pin no. TCIP4 | wire color motorbike | name | description |
| --- | --- | --- | --- | --- |
| orange | 1 | white | IC 1 | inductive coil 1 (cyl 1, 4) |
|  | 2 |  | IC 3 | not connected in standard |
| violet | 3 |  | FUEL PUMPE RELAY | output for fuel pump relay |
| green | 4 |  | M | output for servomotor |
| green | 5 |  | M | output for servomotor |
| grey | 6 |  | TPS | throttle position sensor |
|  | 7 |  |  | not connected |
| black | 8 |  | BLOCK | blocking input |
| yellow | 9 | green/white | CKPS (1) | input for pick-up (1) |
| white | 10 | black/yellow | IC 2 | inductive coil 2 (cyl 2, 3) |
|  | 11 |  | IC 4 | not connected in standard |
|  | 12 |  | GEAR SHIFT LIGHT | output for gear shift light |
| red | 13 | orange | + 12 V | supply 12 V |
| blue | 14 | black | GND | ground |
| green/yellow | 15 |  | TACHO | output for tachometer |
| blue | 16 | black/white | SENSE GND | ground for sensors |
| white/red | 17 |  | + 5 V | supply for sensors |
| white/blue | 18 |  | STPS | servo position sensor |
|  | 19 |  | CLUTCH MASTER | input for gear shift sensor |
| brown | 20 | brown | CKPS (2) | input for pick-up (2) |

Producer address: 	IgniTech

Ceskobratrska 84

535 01 PRELOUC

Czech Republic

ignitech@ignitech.cz

www.ignitech.cz