SPARKER TCIP4 - mounting instructions for Triumph Tiger

Wiring

Wiring must be done according the table below. The wires of ignition SPARKER TCIP4 has various colors. (see table). Counterpart connectors are included.

| wire color TCIP4 | pin no. TCIP4 | wire color motorbike | wire color ignition | name | description |
| --- | --- | --- | --- | --- | --- |
| orange | 1 | brown/yellow | brown | IC 1 | inductive coil 1,4 (use for cyl. 3) |
| yellow/black | 2 | green/white | orange | IC 3 | not connected in standard (use for cyl. 1) |
|  | 3 |  |  | FUEL PUMPE RELAY | output for fuel pump relay |
|  | 4 |  |  | M | output for servomotor |
|  | 5 |  |  | M | output for servomotor |
|  | 6 |  |  | TPS | throttle position sensor |
|  | 7 |  |  |  | not connected |
| black | 8 | grey | grey | INPUT 1 | blocking input (side stand) |
| yellow | 9 | violet | violet | CKPS (1) | input for pick-up (1) |
| white | 10 | yellow/blue | yellow | IC 2 | inductive coil 2,3 (use for cyl. 2) |
|  | 11 |  |  | IC 4 | not connected in standard |
|  | 12 |  |  | GEAR SHIFT LIGHT | output for gear shift light |
| red | 13 | red | red | + 12 V | supply 12 V |
| blue | 14 | black/yellow | white | GND | ground |
| green/yellow | 15 | black/blue | blue | TACHO | output for tachometer |
| blue | 16 | black | black | SENSE GND | ground for sensors |
|  | 17 |  |  | + 5 V | supply for sensors |
|  | 18 |  |  | STPS | servo position sensor |
| grey/red | 19 | light green/white | green | INPUT 2 | blocking input (neutral) |
|  | 20 |  |  | CKPS (2) | input for pick-up (2) |

Producer address: 	IgniTech

Ceskobratrska 84

535 01 PRELOUC

Czech Republic

ignitech@ignitech.cz

www.ignitech.cz