SPARKER TCIP4 - mounting instructions for Yamaha XV500

Wiring

Wiring must be done according the table below. The wires of ignition SPARKER TCIP4 has various colors. (see table). Counterpart connectors are included.

| wire color TCIP4 | pin no. TCIP4 | wire color motorbike | name | description |
| --- | --- | --- | --- | --- |
| orange | 1 | orange | IC 1 | ignition coil 1 |
| yellow/black | 2 |  | IC 3 | ignition coil 3 |
| violet | 3 |  | POWEROUT 1 | multifunctional output 1 |
| green | 4 |  | M | output for servomotor |
| green | 5 |  | M | output for servomotor |
| grey | 6 |  | TPS (IAPS) | throttle position sensor |
| blue | 7 | red | GND, SENSE GND | ground, ground for sensors |
| black | 8 |  | INPUT1 | multifunctional input 1 |
| yellow | 9 | green | CKPS (1) | input for pick-up (1) |
| white | 10 | grey | IC 2 | ignition coil 2 |
| red/black | 11 |  | IC 4 | ignition coil 4 |
| blue/white | 12 |  | POWEROUT 2 | multifunctional output 2 |
| red | 13 | red/white | + 12 V | supply 12 V |
| blue | 14 | black | GND | ground |
| green/yellow | 15 |  | TACHO | output for tachometer light |
| blue | 16 | brown | SENSE GND | ground for sensors |
| white/red | 17 |  | + 5 V | supply for sensors |
| white/blue | 18 |  | STPS | servo position sensor |
| grey/red | 19 |  | INPUT2 | multifunctional input 2 |
| brown | 20 | blue | CKPS (2) | input for pick-up (2) |

Producer address: 	IgniTech

Ceskobratrska 84

535 01 PRELOUC

Czech Republic

ignitech@ignitech.cz

www.ignitech.cz