SPARKER TCIP4 - mounting instructions for Yamaha XVS1100 (2005) and BT1100

Wiring

Wiring must be done according the table below. The wires of ignition SPARKER TCIP4 has various colors. (see table). Counterpart connectors are included.

| wire color TCIP4 | pin no. TCIP4 | wire color motorbike | name | description |
| --- | --- | --- | --- | --- |
| orange | 1 | grey | IC 1 | inductive coil 1,4 |
|  | 2 |  | IC 3 | not connected in standard |
| violet | 3 | black/white, blue/red | FUEL PUMPE RELAY | output for fuel pump relay |
| green | 4 |  | M | output for servomotor |
| green | 5 | green, brown | M | output for servomotor |
| grey | 6 | yellow | TPS | throttle position sensor |
|  | 7 |  |  | not connected |
| black | 8 | blue/yellow | BLOCK | blocking input |
| yellow | 9 | grey | CKPS (1) | input for pick-up (1) |
| white | 10 | orange | IC 2 | inductive coil 2,3 |
|  | 11 |  | IC 4 | not connected in standard |
|  | 12 |  | GEAR SHIFT LIGHT | output for gear shift light |
| red | 13 | red/black | + 12 V | supply 12 V |
| blue | 14 | black | GND | ground |
| green/yellow | 15 | yellow/black (only BT1100) | TACHO | output for tachometer |
| blue | 16 | black/blue | SENSE GND | ground for sensors |
| white/red | 17 | blue | + 5 V | supply for sensors |
| white/blue | 18 |  | STPS | servo position sensor |
|  | 19 |  | CLUTCH MASTER | input for gear shift sensor |
| brown | 20 |  | CKPS (2) | input for pick-up (2) |

Note that there is need to use TCIP4 unit with special firmware.

Producer address: 	IgniTech

Ceskobratrska 84

535 01 PRELOUC

Czech Republic

ignitech@ignitech.cz

www.ignitech.cz